## Slide 1: Final Design presentation
Brenner Craft, Xander Curry, Jacob Miller, Sam Smith
3D Filament Drive
Notes: Jacob

## Slide 2: Overview
Problem Statement
Proposed Solution
Design For:
Tradeoffs
Performance Specifications
Design Evaluation
Predicted Performance
Probability of Success
Schedule
Budget
Next Steps
Notes: Sam

## Slide 3: Problem statement
MEX 3D printers do not account for variation in filament diameter
MTDG believes diameter variation leads to waste
MTDG & BREL want to solve this problem for MEX 3D printers
[1] M. Boulaala, Basic Diagram of FDM 3D Printer Extruder. (a) Direct Extruder. (b) Bowden Extruder. Research Gate, 2020. https://www.researchgate.net/figure/Basic-diagram-of-FDM-3D-printer-extruder-a-Direct-extruder-and-b-Bowden-extruder-15_fig3_376519104
Notes: Brenner

## Slide 4
Excessive Pressure
Insufficient Pressure
Filament Variation
Filament crushed and elongated
Added strain on extruder stepper motor
Filament grinding and slipping
Incorrect amount of material being extruded
Problem Visualization
Constant variations in filament
Severity of variations unpredictable
Notes: Brenner

## Slide 5
Explanation
Filament diameter sensor developed by Thomas Sanladerer
Premade linear rail for force application
Linear potentiometer & limit switch for position detection & closed loop control
1st Model Drawing
Proposed Solution
Initial Concept
Notes: Brenner

## Slide 6
Proposed Solution
1st Prototype
A
Pros & Cons
Pros
Simple design
Position detection system worked well
Cons
Control system unable to measure exact force on filament
Cantilever form led to vibrations
Notes: Brenner

## Slide 7
Main Housing Body
Pressure Arm
Digital End Stop
Linear Potentiometer
Extruder Stepper Motor
Precision Linear Rail
Final Prototype
Mechanical Systems
Mechanical
Custom components 3D printed
  Mounting body for linear rail
  Calibrated pressure arm
  Filament diameter sensor housing/lever
50mm premade linear rail with 0.1mm precision
Printer's stock Nema 17 extruder motor
Notes: Sam

## Slide 8
Main Housing Body
Pressure Arm
Digital End Stop
Linear Potentiometer
Extruder Stepper Motor
Precision Linear Rail
Final Prototype
Electrical Systems
Electrical
Broad sensor array for closed loop control
  Hall-effect sensor
  Digital endstop
  Linear potentiometer
  Strain gauges
PID Loop #1
  Takes diameter reading/needed position & compares to current location
  Sets speed based on difference and moves to needed position
PID Loop #2
  Takes force reading from strain gauge and compares to desired force
  Steps rail forwards or backwards to compensate
Notes: Sam

## Slide 9: Design For- Additive Manufacturing
Maximized use of "free" complexity
Designed for minimal support structure and waste
Optimized component sizing for AM production
Notes: Sam

## Slide 10: Design For- Assembly
Minimized number of components
Designed to align in a single orientation
Installed in printer's pre-existing mounting locations
No specialty tools required
Notes: Sam

## Slide 11: Design For- Safety
Low Voltage
Reduced number of failure modes
Easy accessibility for maintenance and repairs
Open design for visual inspection
Notes: Sam

## Slide 12
Precision
Fast Response Time
Easy Assembly
Small Size & Lightweight
Maximize Lifespan
Importance
PERFORMANCE SPECIFICATIONS
Notes: Brenner

## Slide 13
Specification 1 | Specification 2
Precision | Response Time
Size | Build Difficulty
Precision | Size
Lifespan | Weight
TRADEOFFS
Notes: Sam

## Slide 14
Designing for precision
Leadscrew based actuator
  Common in CNC machines, known for high precision
  Premade linear rail further increases precision
Using closed-loop control
  Values constantly revalidated to determine exact position
  Utilizes variety of sensors:
    Linear potentiometer, limit switch, strain gauges, & hall-effect sensor
[2] "Linear Actuator Stepper Motor for CNC Milling Machine," Amazon. [Online]. Available: https://www.amazon.com/Linear-Actuator-Stepper-Milling-Machine/dp/B07K7FWDZJ?th=1. [Accessed: Dec. 5, 2024].
Predicted Performance
Precision
Notes: Xander

## Slide 15
Designing for Ease of Assembly
Spring mechanism removed
  Less design complexity & easier assembly
All electronics connected to single microcontroller
Connected to pre-existing power supply
  Reduce overall number of parts
Predicted Performance
Easy Assembly
1st Prototype
Revised Prototype
Notes: Xander

## Slide 16
Designing for Fast Response Times
Using Arduino Nano
  Clock speed of 16 MHz
  Processes data faster than filament extrusion
Spring mechanism removed
  Fewer components in compression system ensures faster response time
Actuation System Selection
  Small sized linear rail system operates at sufficient speed and precision
Predicted Performance
Fast response Time
[3] “Arduino Nano,” Arduino Official Store, 2020. https://store.arduino.cc/products/arduino-nano?srsltid=AfmBOoq5md7oHKH53XCXMR7HcQrfkx_0XXJAZi-3u9X6VRjrlWzu-RHk (accessed May 01, 2025).
Notes: Xander

## Slide 17
Designing for Reduced Footprint & Weight
Premade 50 mm linear rail actuator
  Significant weight and size reduction compared to common 100 mm systems
Initial sensor selection changed
  Large load cell bar replaced with smaller strain gauges
Utilizing existing supply-maintained footprint and weight
Predicted Performance
Small Footprint & Lightweight
[4] Culler. Strain Gauge Used in Mechanics Experiment for Material, Industry, or Science. Amazon, n.d., www.amazon.com/dp/B07P8HBPGR.
[5] SparkFun Electronics. Load Cell - 10kg, Straight Bar (TAL220). SparkFun Electronics, n.d., https://www.sparkfun.com/load-cell-10kg-straight-bar-tal220.html. Accessed 1 May 2025.
Notes: Xander

## Slide 18
Designing for Long Lifespan
Inclusion of redundant sensors
  Limit switch and linear potentiometer used for position sensing
Closed-loop control
  Reduces likelihood of mechanical failures
Changed orientation for less stress on Z-axis screw
Predicted Performance
Maximize Lifespan
Notes: Xander

## Slide 19
Maximum Anticipated Variation: 0.1 mm
Minimum Anticipated Variation: 0.025 mm
Linear Rail Precision: Capable of achieving 0.1 mm accuracy without micro stepping
1/32 Micro step driver that gives maximum theoretical precision of 0.003mm
Outcome: Success
Micro step drive provided 0.003mm precision
Linear potentiometer provided absolute position data to account for backlash
[6] James, S. P., & Prawel, D. A. (n.d.). Biomaterials Research and Engineering Laboratory (BREL). Colorado State University, Department of Mechanical Engineering. Retrieved May 1, 2025, from
Probability of Success
Precision
Notes: Jacob

## Slide 20
No specialty tools required
No specialty manufacturing
  4 unique 3D printed parts
  Off the shelf components
Outcome: Success
Total parts: 47, including all mounting hardware
Simple assembly: Easy setup for user
Probability of Success
Easy Assembly
Notes: Jacob

## Slide 21
Print Speed & Extrusion Rates (CURA slicer, 0.4 mm nozzle):
Print speed: 40-100 mm/s (typical range).
Extrusion rate: 3.84-9.60 mm³/s.
Linear filament speed:
  At 40 mm/s print speed: 1.6 mm/s.
  At 100 mm/s print speed: 4.0 mm/s.
Linear rail system: Maximum speed of 40 mm/s under a 3 kg load
Outcome: Success
Max linear speed of filament never greater than actuation speed
Compares measurements in both PID loops & actuate within 30 ms
Probability of Success
Fast Response Time
Notes: Jacob

## Slide 22
Rotated device to be parallel with gantry bar
Current Weight of Gantry Bar: 800 - 1000 grams
Additional Weight of Assembly: 500 grams
Theoretical Lift Capacity of NEMA 17 Motor: 7,000 - 8,000 grams
Outcome: Success
Device fits inside printer footprint and does not weigh enough to damage Z stepper
[7] "3D Printable Ender 3 V2 Upgrade," Thingiverse. [Online]. Available: https://www.thingiverse.com/thing:6691542. [Accessed: Dec. 5, 2024].
Probability of Success
Small Footprint & lightweight
Notes: Jacob

## Slide 23
Redundant sensors and closed-loop control prevent collisions
Additional support attached to gantry bar reduces moment on Z – axis lead screw
  Reduces vibrations from cantilever design
Outcome: Success
No collisions observed in testing
No change in vibrations with device
Probability of Success
Maximize Lifespan
Notes: Jacob

## Slide 24
Static Extruder Key Points:
Sporadic changes in force
Mean: 10.84 N, Variance: 0.893 N, Range: 6.51 N
Prototype Extruder Key Points:
Consistent force band
Mean: 10.50 N, Variance: 0.706 N, Range: 5.33 N
Data & Results
Force Testing
Notes: Sam

## Slide 25
Budget
Total Spent: $2,659.29 ≈ 60% of total budget
$1,300 spent on 3d Printers & Filament
Total Prototype Cost: $122.57
Linear rail accounts for 50% of prototype cost
Notes: Xander

## Slide 26
Finished System
(EDAYS)
Vibration Testing
Final Prototype
Control System Prototype
Alpha Mechanical Prototype
Start of Semester
1st 4 weeks
2nd 4 weeks
3rd 4 weeks
Finalized Control System
Mechanical System Prototype
Force Test System
Alpha Control System
Critical Path Flowchart
Notes: Brenner

## Slide 27
Gantt Chart
Notes: Jacob

## Slide 28
NEXT steps
Future Work
Integration with other BREL systems
Print quality & lifecycle testing
Custom fabrication to further reduce footprint
Adapt device for more advanced printers
Notes: Xander

## Slide 29: Conclusion
Problem Statement
Proposed Solution
Design For _____
Tradeoffs
Design Evaluation
Predicted Performance
Probability of Success
Schedule
Budget
Notes: Sam

## Slide 30: Questions?
Thank you
Notes: Jacob

## Slide 31
Picture Sources
Semester 1 Gantt Chart
Semester II Gant Chart
Hose of Quality
BOM
Detail Drawings
Assembly Drawing
Appendix

## Slide 32
[1] M. Boulaala, Basic Diagram of FDM 3D Printer Extruder. (a) Direct Extruder. (b) Bowden Extruder. Research Gate, 2020. https://www.researchgate.net/figure/Basic-diagram-of-FDM-3D-printer-extruder-a-Direct-extruder-and-b-Bowden-extruder-15_fig3_376519104
[2] "Linear Actuator Stepper Motor for CNC Milling Machine," Amazon. [Online]. Available: https://www.amazon.com/Linear-Actuator-Stepper-Milling-Machine/dp/B07K7FWDZJ?th=1. [Accessed: Dec. 5, 2024].
[3] “Arduino Nano,” Arduino Official Store, 2020. https://store.arduino.cc/products/arduino-nano?srsltid=AfmBOoq5md7oHKH53XCXMR7HcQrfkx_0XXJAZi-3u9X6VRjrlWzu-RHk (accessed May 01, 2025).
[4] Culler. Strain Gauge Used in Mechanics Experiment for Material, Industry, or Science. Amazon, n.d., www.amazon.com/dp/B07P8HBPGR.
[5] SparkFun Electronics. Load Cell - 10kg, Straight Bar (TAL220). SparkFun Electronics, n.d., https://www.sparkfun.com/load-cell-10kg-straight-bar-tal220.html. Accessed 1 May 2025.
[6] James, S. P., & Prawel, D. A. (n.d.). Biomaterials Research and Engineering Laboratory (BREL). Colorado State University, Department of Mechanical Engineering. Retrieved May 1, 2025, from
[7] "3D Printable Ender 3 V2 Upgrade," Thingiverse. [Online]. Available: https://www.thingiverse.com/thing:6691542. [Accessed: Dec. 5, 2024].
Picture Sources

## Slide 33
Original Schedule
Notes: Jacob

## Slide 34
Beginning of 2nd Semester Schedule
Notes: Jacob

## Slide 35
House of quality

## Slide 36
Final Bill of materials 1

## Slide 37
Final Bill of materials 2

## Slide 38
Detail Drawing
Wiring Diagram

## Slide 39
Detail Drawing
Pressure arm

## Slide 40
Detail Drawing
Mounting Bracket

## Slide 41
Detail Drawing
Electronics Housing

## Slide 42
Detail Drawing
Exploded View

## Slide 43
Extra Pictures
AA